## Slide 1: Enhanced Low SNR Radio Signal Classification using Deep Learning
M Farhan Tandia (0860814),
Ivan Surya H (0860812) - 3
National Chiao Tung University, Taiwan
AI Wireless
Final Presentation

## Slide 2
Background
Signal modulation used to transmit a signal is important. Spectrum interference monitoring, radio fault detection, dynamic spectrum access, etc.
Traditional signal classification need to extract some features. Fourier Transform, SIFT, MFCC, or another handcrafting method using statistical modulation features.
Defense Application Radio signals may reveal vital information regarding the detection, localization, and identification of an opponent. Traditionally, operators who were trained to recognize various signal formats based on manual ‘listen in’ techniques performed the identification.

## Slide 3
Problem
What is the new state of the art of deep learning needs to be chosen and suitable for radio signal classification?
How we could make use of a large dataset to classify the RAW signal using the new state of the art of deep learning network?
How we could do a benchmark comparison with the previous state of the art method?
Notes: Problems
What are the problems that you are trying to solve?
Why are the problems important?

## Slide 4
Challenges
In reality, the signal is always not ideal and combined with unwanted signal that is considered as noise. In the image below, we can see how drastically noise can affect our ability to recognize a signal.
A clean signal will have a high SNR and a noisy signal will have a low SNR. We should be able to classify signals both in low SNR and high SNR.
We use the DeepSig Radio Signal Dataset, this dataset is pretty large (18GB). We will use 1.5 Million variation of signal modulation with respect to the SNR value.
DeepSig Dataset
High VS Low
SNR
Notes: Challenges
What are the limitation of current approaches?
What are the differences between these prior approaches and your proposed?

## Slide 5
Goal
      Our target is to get higher accuracy in lower SNR value. It will indicate that our model is robust under the noisy signal modulation.
We will design a new deep learning architecture and try to get the comparable results in terms of accuracy with state of the art or even better.
Our deep learning model will work using only RAW signal without the need preprocessing or denoising the noisy signal.
Increase Low SNR
Classification Accuracy
Get a comparable result
on High SNR Classification
Accuracy.
Notes: Goal
What is your key concept and its unique and novelty?
What are the expected advantages?

## Slide 6
Method
Notes: Goal
What is your key concept and its unique and novelty?
What are the expected advantages?

## Slide 7
Key Result (Resnet)

## Slide 8
Key Result (Transformer)

## Slide 9
Key Result (Ensemble)

## Slide 10: Thank you


## Slide 11
Key References
T. J. O’Shea, T. Roy and T. C. Clancy, "Over-the-Air Deep Learning Based Radio Signal Classification," in IEEE Journal of Selected Topics in Signal Processing, vol. 12, no. 1, pp. 168-179, Feb. 2018, doi: 10.1109/JSTSP.2018.2797022.
J. Uppal, M. Hegarty, W. Haftel, P. A. Sallee, H. Brown Cribbs and H. H. Huang, "High-Performance Deep Learning Classification for Radio Signals," 2019 53rd Asilomar Conference on Signals, Systems, and Computers, Pacific Grove, CA, USA, 2019, pp. 1026-1029, doi: 10.1109/IEEECONF44664.2019.9048897.
S. Huang et al., "Automatic Modulation Classification Using Compressive Convolutional Neural Network," in IEEE Access, vol. 7, pp. 79636-79643, 2019, DOI: 10.1109/ACCESS.2019.2921988.
Huynh-The, Thien & Hua, Cam-Hao & Pham, Quoc-Viet & Kim, Dong-Seong. (2020). MCNet: An Efficient CNN Architecture for Robust Automatic Modulation Classification. IEEE Communications Letters. 24. 811-815. 10.1109/LCOMM.2020.2968030.